STAAD SPACE

START JOB INFORMATION

ENGINEER DATE 14-May-09

END JOB INFORMATION

INPUT WIDTH 79

UNIT METER KN

JOINT COORDINATES

1 0 0 0; 2 8 0 0;

MEMBER INCIDENCES

1 1 2;

DEFINE MATERIAL START

ISOTROPIC STEEL

E 2.05e+008

POISSON 0.3

DENSITY 76.8195

ALPHA 1.2e-005

DAMP 0.03

END DEFINE MATERIAL

MEMBER PROPERTY AMERICAN

1 TABLE ST W18X35

CONSTANTS

MATERIAL STEEL ALL

SUPPORTS

1 2 FIXED

LOAD 1 LOADTYPE None  TITLE DEAD LOAD

MEMBER LOAD

1 CON GY -10 4

LOAD 2 LOADTYPE None  TITLE ACCEL Z

MEMBER LOAD

1 CON GZ 3 4

LOAD COMB 3 1.3DL

1 1.3

LOAD COMB 4 1.3DL+0.7ACCL

1 1.3 2 0.7

LOAD COMB 5 1.0DL+1.3ACCL

1 1.0 2 1.3

PRINT PROBLEM STATISTICS

PERFORM ANALYSIS PRINT ALL

PRINT ANALYSIS RESULTS

FINISH

# Text boxes

Load case 4

Load 4

For same load cases different BM diagrams????