## Slide 1
The task:
Model a bulkhead consisting of deep primary girders, shallow stiffeners, and plates.
Beams are offset to simulate the eccentricity of stiffeners and plate.
Offset also allows for all nodes to be on the same plane (the plates plane).
Code check the beams – buckling being the main concern.

## Slide 2
Model info:
Primary girders UB914x305x253.
Stiffeners UB254x146x31.
Plate 10mm thick.
Z-direction offsets applied to bring all items flush at the plate nodes.
1000kN vertical nodal load applied at the top of each of the three girders.
AISC ASD code check applied.

## Slide 3
Results:
It seems like the axial force in the beam is far too low, only containing 320kN (32%) of the 1000kN input load.
Can it really be that STAAD is sending the other 68% of the load through the plates only? It does not seem right.
Code check results also seem suspiciously low at the centre segments.
Therefore, I created some copies of the model to test different settings, see next slides.

## Slide 4
Model 1:
Original version
Model 2:
Beams with offset
No plates
Model 3:
No offsets – all items modelled at centroids
Plates included
Model 4:
No offsets – all beams modelled at centroids
No Plates
All other details are the same.

## Slide 5
Model 1:
Axial load 320kN
Model 2:
Axial load 1000kN
Model 4:
Axial load 1000kN
Model 3:
Axial load 561kN

## Slide 6
Model 1
Model 2
Model 4
Model 3
Code check results

## Slide 7
Perhaps a better way to show the strange behaviour with the axial forces being affected by plates – is the deck version.
Model 5
Model 6
Model 7

## Slide 8
Properties are all the same except now the girders are simply supported and the point load is applied at the mid-span.

## Slide 9
With beams offset and plates present, STAAD reports a huge axial tension.
Beams offset but no plates = okay
Beams not offset and plates included = okay.
It should be noted that if the external load is upwards rather than downwards, the beams will show massive compression instead, and this usually affects the code check result. Is it real? Or simply a bad way to use STAAD?